| Pos | Name | Comments |
| --- | --- | --- |
| 1 | Hydraulic modulator |  |
| 2 | Brake line connection | for right brake caliper |
| 3 | Brake line connection | for left brake caliper |
| 4 | Brake line connection | for brake pressure regulator |
| 5 | Pressure regulator valve | opens to rear axle starting at 8 bar, cannot be checked in shop |
| 6 | Cap |  |
| 7 | Brake fluid reservoir |  |
| 8 | Sleeve | always replace |
| 9 | O-ring | always replace |
| 10 | Sealing plug | always replace |
| 11 | Reservoir mounting retainer |  |
| 12 |  | 10 Nm (7 ft lb) |
| 13 | Pressure accumulator | 45 Nm (33 ft lb), coat o-ring with brake fluid before installing |
| 14 | O-ring | always replace, coat with brake fluid before installing accumulator |
| 15 | Brake line | pump to modulator |
| 16 | Hydraulic pump |  |
| 17 | Connecting hose |  |
| 18 | Pressure warning switch | 25 Nm (18 ft lb), coat o-ring with brake fluid before installing |
| 19 | O-ring | always replace |
| 20 | Bracket |  |
| 21 |  | 25 Nm (18 ft lb) |
| 22 |  | 25 Nm (18 ft lb) |
| 23 | Seal |  |
| The following components of the ABS hydraulic modulator assembly can be replaced: |
|  | hydraulic modulator |  |
|  | reservoir |  |
|  | pressure-warning switch |  |
|  | pressure accumulator |  |
|  | pump subassembly |  |
| Before the hydraulic modulator assembly is removed, check pump assembly and pressure warning switch |
|  | to check: reduce pressure in accumulator, turn ignition on, pump must start running and shut off after a maximum of 60 seconds, depress brake pedal 2 or 3 times: pump must start running again |
| WARNING! |  |
|  | The ABS modulator assembly is capable of "self-pressurizing" up to 210 bar (3045 psi). Serious injury may result if you service the unit without properly depressurizing it. Depress brake pedal 25 to 35 times with ignition switch in OFF position, to depressurize system. |